## Slide 1
2024 IEEE International Conference on Artificial Intelligence Circuits and Systems
Reusing Softmax Hardware Unit for GELU Computation in Transformers
Electrical and Computer Engineering
Democritus University of Thrace, Greece
Christodoulos Peltekis, Dionysios Filippas, Giorgos Dimitrakopoulos

## Slide 2
Transformer Applications
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
Natural Language Processing
Text-to-Image Transformation
Recommendation Systems
Drug Discovery

## Slide 3
Inside a Transformer
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
Proj.
Proj.
Proj.
MatMul
Softmax
MatMul
Add & LayerNorm
Fully Connected
GELU
Fully Connected
Q
K
V
Input embedding
Multi-head Self-Attention
Add & LayerNorm
Feed – Forward
Encoder block
Two activation functions
Activation functions have significant proportion of the total runtime
How to extend the reusability of custom hardware units like softmax?
Custom hardware softmax units are common

## Slide 4
Softmax Activation Function
Receives an N-element input vector
Produces an N-element vector of probabilities as output
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
Subtract the maximum value of vector  all exponent inputs have zero or negative values  more stable result

## Slide 5
Move to Logarithm Domain for Hardware Softmax
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
>
>
>
-
-
exp
exp
Max tree
xi – max(x)
exi - max
Adder tree
Σ(exj – max(x))
-
-
exp
exp
log
xi – max(x) – log(Σ)
log(Σ(exj – max(x)))
exi – max(x) – log(Σ)
+
+
+
y1
yN
xN
x1
x2
Perform division in logarithm domain
Better fit for hardware
Moving to logarithm domain transforms division to a simple subtraction

## Slide 6
SIMD Softmax Unit
Enhance classic softmax unit with minimum extra hardware cost
Two operation modes:
  Normal  compute a single N-element output vector
  GELU  compute N/2 two-element output vectors
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
>
>
>
-
-
exp
exp
-
-
exp
exp
log
log
log
0
1
1
0
mode
0: GELU
1: Normal
0
1
1
0
+
+
+
mode
y1
yN
xN
x1
x2
max of every pair of inputs
Sum of every pair of inputs
SIMD - Softmax
Dual – mode Softmax
x1
x2
xN-1
xN
y1
y2
yN-1
yN
x3
x4
y3
y4
Either compute a full-length vector or multiple smaller
Either compute a full-length vector or multiple smaller

## Slide 7
GELU Activation Function
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
Error function in GELU computation could be approximated by a tanh [1]
[1] D. Hendrycks and K. Gimpel, “Gaussian Error Linear Units (GELUs),” arXiv preprint arXiv:1606.08415, 2016.

## Slide 8
Reusing Softmax Operator for GELU
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
k
Reuse softmax unit to compute GELU with a two-element vector as input

## Slide 9
Combined GELU-Softmax Unit
Use a polyonym to compute k values
Reuse Dual-mode softmax unit to compute GELU outputs
This unit could either compute softmax output for N-element vectors or N/2 GELU outputs
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
kN/2
-k1
SIMD - Softmax
z1
k1
1
0
mode
1
0
N/2 GELU outputs
1
0
0
1
-kN/2
1
0
0
1
z2
zΝ-1
zΝ
x1
x2
xN-1
xN
y1
y2
yN-1
yN
z1
zN-1
mode
a(z+bz3)
a | 
b | 
a | 
b | 
a(z+bz3)

## Slide 10
Experimental Setup
Evaluations are twofold, aiming to highlight that proposed GELU
  Does not affect the accuracy of BERT model in well-known benchmarks of the GLUE dataset
  Saves area and power compared to state-of-the-art integer GELU architectures
Two configurations are under comparison
  Proposed GELU unit with SIMD softmax
  Classic Softmax unit with N/2 i-GELU units
Designs implemented in C++ and synthesized to Verilog RTL using Catapult HLS
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
Same degree of available parallelism

## Slide 11
Accuracy Performance
Both methods achieve equivalent accuracy with the fully accurate “FP32” model
Proposed GELU implementation outperforms i-GELU in terms of Mean Absolute Error compared to fully accurate model
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
 |  | STS2 | MNLI-m | MNLI-mm | QQP | QNLI | CoLA | MRPC | RTE
Accuracy (%) | FP32 | 92.7 | 79.1 | 84.2 | 90.8 | 94.1 | 72.4 | 85.8 | 73.8
 | i-GELU | 92.4 | 79.0 | 84.0 | 90.7 | 94.1 | 72.1 | 86.6 | 73.7
 | Proposed | 92.5 | 79.1 | 84.1 | 90.7 | 94.0 | 72.3 | 85.7 | 73.8
Mean Absolute Error | i-GELU | 0.054 | 0.0824 | 0.094 | 0.098 | 0.064 | 0.076 | 0.1204 | 0.179
 | Proposed | 0.0039 | 0.0057 | 0.0061 | 0.0083 | 0.0045 | 0.0067 | 0.0109 | 0.0154

## Slide 12
Hardware Overhead of SIMD-Softmax
Marginal hardware overhead on softmax unit to support multiple input vector lengths
The proposed implementation is scalable to large input vectors
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
N | Area (μm2) |  |  | Power (mW) |  | 
 | Single mode | Dual mode | Difference | Single mode | Dual mode | Difference
8 | 92309 | 100675 | 9.1% | 13.51 | 13.95 | 3.3%
32 | 363703 | 403025 | 10.8% | 57.74 | 58.84 | 1.9%

## Slide 13
Area and Power Reduction
The two designs configured to have equal computation throughput
Proposed GELU implementation outperforms the alternative in both required area and power
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh
8.4%
10.7%
3.8%
13.2%

## Slide 14
Conclusions
Enhance state-of-the-art softmax hardware unit to reconfigurably support multiple vector lengths
Implement a GELU unit that reuses the SIMD softmax unit
Proposed GELU computation preserves the same accuracy compared to fully accurate floating-point model
Reduce area and power consumption compared to state-of-the-art alternatives
Christodoulos Peltekis - Integrated Circuits Lab @ DUTh